## Slide 1: High Speed Networks and Switching
Mininet Final Project: Test & Analyze Packet Switching Algorithms as a Load-Balancing Method
Assigned by: Eyal Zvi, 319067732 Efi Korenfeld, 208838359 Saar Ben-Yochana, 313234155

## Slide 2: Introduction
With the ongoing increase of users online, one of the major factors of network efficiency is congestion control
Many service providers try to solve this problem by using load balancing algorithms when the main goal is to minimize service time and reduce congestion in each server individually
In this project we will simulate and compare different scheduling algorithms in order to determine which of the algorithms tested is optimal for each scenario

## Slide 3: Implementation
Simulation environment – Mininet
Algorithms – RR, Random, WFQ (pre-defined weights)
Model – Clients send HTTP Requests to a load balancing node that decides according to the algorithm tested which server handles the request
Measurements - Clients collect and record response time measurements according to the received HTTP replies
Control – A worst case scenario is tested where the slowest server receives all HTTP Requests

## Slide 4: Test Cases
Topology 1: 3 Clients vs. 3 Servers - All servers with equal service times

## Slide 5: Test Cases
Topology 1: 3 Clients vs. 3 Servers - Servers with different service times

## Slide 6: Test Cases
Topology 2: 6 Clients vs. 3 Servers - All servers with equal service times

## Slide 7: Test Cases
Topology 2: 6 Clients vs. 3 Servers - Servers with different service times

## Slide 8: Results
RR is the optimal algorithm
WFQ and Random algorithms are almost equally efficient

## Slide 9: Results
WFQ is the optimal algorithm
Although RR is not destined for unequal weighted servers it functions well and is relatively stable

## Slide 10: Results
RR is the optimal algorithm
Note that Random algorithm overtakes WFQ

## Slide 11: Results
WFQ is the optimal algorithm
Note that Random algorithm overtakes RR

## Slide 12: Conclusions
According to our model and simulation results:
WFQ is optimal1 for servers with different service times
Given identical service times the optimal algorithm is RR
As the number of clients increase the Random algorithm shows more efficiency and becomes the 2nd optimal choice
We conclude that when the topology and weights are known it is most efficient using RR or WFQ according to the ratio between server weights. Otherwise, using the Random algorithm can result in higher efficiency than choosing one of the other algorithms.
[1] - Given that the weights are properly assigned

## Slide 13: Thank You!